## Slide 1
HARDWARE MOUNTING AND CABLE GUIDE
HEAVY DUTY VEHICLE (U.S.)
CHEVROLET SONIC

## Slide 2
Year Range | SR4 Harness Description | SR4 SKU | Cable Type
2012-2020 | Driver-side ODBII 16-pin black | 104-0009-0013-00 | 
Chevrolet Sonic
Cable Guide
2019 Chevrolet Sonic
(Flat Windshield)

## Slide 3
Note: Any combination of these mounting locations are approved
Chevrolet Sonic (all years)
Approved camera mounting (flat windshield), sensor bar, and keypad locations
Sensor Bar
Bottom A-pillar
Forward Cam
center windshield
Keypad
Right of steering wheel
Forward Cam
center windshield
Keypad
Left of steering wheel
Flat windshield - Preferred locations
Flat windshield - Alternative locations
Sensor Bar
Bottom A-pillar
Sensor Bar
Middle A-pillar
Cab Cam
Right of Forward Cam
Cab Cam
Left of Forward Cam

## Slide 4
Component | Primary location | Secondary location
Controller | Center Dash Rear of center dash. Right of gas pedal behind panel near floor. | Same
ECU Port | Driver-side OBDII, 16 Pin, (black) (104-0009-0013-00) | Universal 3-Wire (No Data Link Connector DLC) (104-0009-0001-00) Use when DLC is used by a third party device
Wiring Constant Power | Driver-side Fuse box under the dash | Same
Wiring True Ignition | Driver-side Fuse Box under the dash | Same
Wiring Ground | Driver-side Chassis at door jamb | Same
1
2
Chevrolet Sonic
2012-2020 YEARS
Approved controller, ECU, and wiring locations
Primary
1
1
FUSE
BOX
+12v Constant
+12v True Ignition
(Chassis) Ground

## Slide 5
Key Compliance Specifications
Forward-facing Camera
Mount the camera within 6" from the top of the windshield.
Camera cannot interfere with a driver’s line of sight
to the road, traffic signals, or road signs
Cab-facing Camera
Camera lens must have a complete view of the driver when the visors are in the down and fully extended position. Use a headliner location
when the fully extended visor covers the camera lens.
Make sure the cab-facing camera bracket, or vehicle's headliner, DOES NOT BLOCK the cameras Infrared (IR) sensors
Top Infrared Sensor
Bottom Infrared Sensor
Infrared Sensor is obstructed by the bracket

## Slide 6
Key Compliance Specifications
Master Power Cutoff (MPC) and Low Voltage Disconnect (LVD)
Connect the SmartRecorders Red Constant Power wire to the Hot/Battery side of the Master Power Cut-off switch.
Connect the SmartRecorders Red Constant Power wire to the Positive Post of the Vehicles Battery.
Connect the SmartRecorders Red Constant Power wire to the Hot/Battery of side the Low Voltage Disconnect.
The SmartDrive SR4 system is designed to function only with a Positive MPC/LVD, not a Negative Ground MPC/LVD.