## Slide 1
HARDWARE MOUNTING AND CABLE GUIDE
HEAVY DUTY VEHICLE (U.S.)
FORD F150-F550

## Slide 2
Year Range | SR4 Harness Description | SR4 SKU | Cable Type
1996-2020 | ODBII 16-pin black | 104-0009-0013-00 | 
Ford F150-F550
Cable Guide
Ford F-450
(Flat Windshield)
Ford F-150
(Flat Windshield)

## Slide 3
Sensor Bar
Bottom A-pillar
Forward Cam
center windshield
Cab Cam
Left of Forward Cam
Keypad
Right of steering wheel
Forward Cam
center windshield
Keypad
Left of steering wheel
Note: Any combination of these mounting locations are approved
Flat windshield - Preferred locations
Flat windshield - Alternative locations
Sensor Bar
Bottom A-pillar
Sensor Bar
Middle A-pillar
Cab Cam
Right of Forward Cam
Ford F150-F450 (all years)
Approved camera mounting (flat/split windshield), sensor bar, and keypad locations

## Slide 4
Component | Primary location
Controller | Driver-side Under steering column
ECU Port | Driver-side ODBII, 16-pin black (104-0009-0013-00)
Wiring Constant 12V power & true ignition | Driver-side fuse box Engine Compartment
Wiring Ground | Passenger-side Behind kick panel
1
Ford F150
2010-2020 Approved controller, ECU, and wiring locations
Primary
1
1
+12v Constant
+12v True Ignition
Fuse Box Engine Compartment
(Chassis) Ground

## Slide 5
Component | Primary location
Controller | Driver-side Behind the instrument panel
ECU Port | Driver-side ODBII, 16-pin black (104-0009-0013-00)
Wiring Constant Power | Driver-side Positive (Hot) side of the battery
Wiring True Ignition | Passenger-side Fuse Box behind kick panel
Wiring Ground | Passenger-side Ground post near fuse box
1
Primary
1
1
+12v True Ignition
Ford F250
2013-2020 Approved controller, ECU, and wiring locations
FUSE
BOX
+12v Constant
(Chassis) Ground
BATTERY

## Slide 6
Key Compliance Specifications
Forward-facing Camera
Mount the camera within 6" from the top of the windshield.
Camera cannot interfere with a driver’s line of sight
to the road, traffic signals, or road signs
Cab-facing Camera
Camera lens must have a complete view of the driver when the visors are
in the down and fully extended position. Use a headliner location
when the fully extended visor covers the camera lens.
Make sure the cab-facing camera bracket, or vehicle's headliner, DOES NOT BLOCK the cameras Infrared (IR) sensors
Top Infrared Sensor
Bottom Infrared Sensor
Infrared Sensor is obstructed by the bracket

## Slide 7
Key Compliance Specifications
Master Power Cutoff (MPC) and Low Voltage Disconnect (LVD)
Connect the SmartRecorders Red Constant Power wire to the Hot/Battery side of the Master Power Cut-off switch.
Connect the SmartRecorders Red Constant Power wire to the Positive Post of the Vehicles Battery.
Connect the SmartRecorders Red Constant Power wire to the Hot/Battery of side the Low Voltage Disconnect.
The SmartDrive SR4 system is designed to function only with a Positive MPC/LVD, not a Negative Ground MPC/LVD.